## Slide 1: Advancing Digital Supply Chains in Construction Products through Standardisation
Finnish Association of Construction Products Industries
Teemu Alaluusua
2025-10-07 / Digital Construction Workshop – Construction Products Europe

## Slide 2: Contents
Production strategies point of view for development
Current state of digital supply chain management, Engineer-to-Order Precast Concrete
Development Roadmap
  Standards to Follow in Supply Chain Digitalization
  Developed Implementation Guidelines for Supply Chain Data Exchange
  Future state data flow architecture, Engineer-to-Order Precast Concrete
2

## Slide 3
Product Manufacturing
The figure depicts the value chain of the construction project (↓) and the supply chain of the construction products linked to it (→)
Production chains in the construction industry
Material Extraction & Delivery
Supplier
Product Supply Chain
Value chain of the construction project
Design
Costing & Approvals
Procurement
Project developer
Delivery
Project Consideration
Contractor
Architects, Structural engineers, MEP-designers
On-Site Assembly
Operation
FM
. . . .
Demolition
. . . .
. . . .
Manufacturer
PRODUCTION STRATEGY PERSPECTIVE ON DEVELOPMENT
3

## Slide 4
Assembly
Product design
Parts manufacturing
Assembly
Parts manufacturing
Product design
Storage
The production strategy determines the customer order decoupling point, illustrating where production control transitions from push to pull across MTS, ATO, MTO, and ETO models.
Material Extraction & Delivery
Supplier
Product Supply Chain
Product design
Parts manufacturing
Assembly
Storage
Value chain of the construction project
Design
Costing & Approvals
Procurement
Project developer
Delivery
Project Consideration
Contractor
Architects, Structural engineers, MEP-designers
On-Site Assembly
Operation
FM
. . . .
Demolition
. . . .
. . . .
Manufacturer
Product Manufacturing
Engineer-to-
Order
Make-to-
Order
Assembly-to-
Order
Make-to-
Stock
Production chains in the construction industry
4

## Slide 5
Engineer-to-
Order
Make-to-
Order
Assembly-to-Order
Make-to-
Stock
Production strategies for building products
BETONI
Delivery
Project-specific products
Standard products
In Finland, we are currently working on the precast concrete supply chain as an Engineer-to-Order reference case
5
Notes: The development work in Finland is carried out in supply chain work groups, which are divided according to the production strategies.
In Finland, we are currently working on the precast concrete supply chain as an Engineer-To-Order reference case.

## Slide 6
Current State
Development roadmap
Future State
Current State
(Based on preliminary studies & workshops results )
Fig 1. Alhava, O (2023)
Fig 2. Alaluusua, T (2023)
BIM data is not usable across the supply chain.
Lack of linked building data prevents seamless information flow between stakeholders.
Current data architecture is based on closed information exchange systems.
  Point-to-point, customized integrations are inefficient and costly.
Lack of interoperability between systems and platforms.
Unstructured data (PDFs, images, phone calls, emails) dominates communication, making automation and analytics difficult.
Ref. Alaluusua, T. (2023) Digital management of information exchange in takt production supply chains
Ref. Alhava et al. (2024) Challenges and Opportunities in Digitalising Concrete Element Supply Chain: Proposed National Model
Notes: The development project was initiated through preliminary studies conducted on construction sites, followed by a series of supply chain workshops involving industry experts. The aim was to map the current processes of the precast concrete element supply chain — covering all stages from design to installation — and to identify issues occurring in different parts of the chain.
During these workshops, each stage of the process was analyzed, including the stakeholders involved, the current methods and formats of information exchange, and the challenges encountered.
The key findings were related to the flow of information between different phases of the supply chain.

## Slide 7
Current State
Development roadmap
Future State
Development Roadmap
public authorities
Academia
Industry practitioners
IT
companies
Non-profit associations
Based on the current state analysis, we developed a general development roadmap that covers all production strategies.
Our findings show that advancing digital supply chains requires the comprehensive development of operations, information management, and technology systems.
To achieve the best results, we collaborate with experts from various organizations, including academia, industry practitioners, non-profit associations, public authorities, and IT companies.
Notes: Based on the current state analysis, we developed a general development roadmap that covers all production strategies.
Our findings show that advancing digital supply chains requires the comprehensive development of operations, information management, and technology systems.
To achieve the best results, we collaborate with experts from various organizations, including academia, industry practitioners (manufacturers, contractors, designers), non-profit associations, and public authorities such as the State Treasury, the Ministry of the Environment, and the Finnish Tax Administration, as well as IT companies.

## Slide 8: Development Roadmap
Reference data for design
(data dictionaries)
Order-delivery process
Peppol, EPCIS, eFTI
Product data process:
GS1 standards
Design process:
Data dictionaries, reference data
(FI) Strategic objective
Digitalised way of working in construction
The procurement process: Company's own ERP/data platform
Engineering Bill of Materials (EBOM) from the building’s BIM model
Redrawn from: CC-BY 4.0: Arola, T., Alhava, O., June 12, 2024: Digitalization of the Construction Industry: Supply Chain Digitalization, RYHTI and Interoperability (presentation)
Digital, message based supply chain process
(PEPPOL / EPCIS / eFTI)
Adoption of AI-based processes
Digital takt-production management
E-supply chain management
Automatic calculation of the actual carbon footprint
Automated calculation of the carbon footprint of building design
As-built data collection and digital delivery
Automated GWP and sustainability reporting
Implementing circular economy processes
Automatic calculation of transport carbon footprint
Digitalisation 1.0:
Digitising current construction processes
Unique Product Identification + Data Carriers
Product information sharing in machine-readable format
(According to ETIM & (FI) TT-standard)
Manufacturing Bill of Materials (MBOM) of the building
Digitalisation 2.0:
Digitalisation of responsible construction and the use of modern technology
8
Notes: About the Development Roadmap Framework for the Digitalisation of Construction Supply Chains
This figure presents the action points of current construction processes that represent Digitalisation 1.0 — the foundation that must be addressed to enable Digitalisation 2.0, focusing on responsible construction and the use of modern technologies.
The roadmap covers several process areas:
Design process: Establishing reference data for design and ensuring export of relevant information forward along the supply chain.
Product data process: Applying GS1 identification and data capture methods and enabling machine-readable product information sharing.
Procurement process: Combining product and design data to generate the manufacturing Bill of Materials (mBOM).
Order and delivery process: Standardising data exchange using formats such as Peppol, eFTI, and EPCIS.
By implementing these actions, we can achieve a more digitalised and data-driven way of working in construction.

## Slide 9: Standards to Follow in Supply Chain Digitalization
LOIN
Level Of Information Need
EN ISO
7817-1:2024
Peppol / UBL
EN ISO/IEC
19845:2015
Information management
Processes – how to work in the project using BIM
EN ISO
19650-1:2018
EN ISO
19650-2:2018
EN ISO
19650-3:2020
EN ISO
19650-4:2022
EN ISO
19650-5:2020
CEN/TR
17439:2020
IFC
Data model –schema and format
EN ISO
16739:2024
Data templates, properties
EN ISO
22057:2022
EN ISO
23387:2020
EN ISO
23386:2020
IFD classification, SML
Data dictionaries, classification, linked data
EN ISO
12006-2:2020
EN ISO
12006-3:2022
eFTI (EU)
CELEX
32020R1056
EPCIS (GS1)
GS1 EPCIS Standard:2022
GS1 CBV Standard:2022
GS1 EPCIS & CBV Guideline:2023
EU DPP
XXXX XXXXX
-
EN ISO/IEC
16931-1:2017
Identification
GS1 GLN
ISO/IEC 6524
GS1 SSCC
ISO/IEC 15459-1 ISO/IEC 6523
GS1 GIAI
ISO/IEC 15459-4 & 5 ISO/IEC 6523
GS1 GSRN
ISO/IEC 15418
GS1 GRAI
GS1 GDTI
GS1 GTIN
ISO/IEC 15459-6
ISO/IEC 6523
Data Capture
GS1 Data Matrix
ISO/IEC 16022
GS1 QR Code
ISO/IEC 18004
EPC Tag Data Standard
ISO/IEC 15962:2024
EAN/UPC barcode
ISO/IEC 15420
GUID / UUID
ISO/IEC
9834-8:2005
ISO/IEC
11578:1996
EPD
EN ISO
14025:2018
Order-delivery process
GS1 Standards
Notes: From interoperability point of view, it is important to be aware of existing standards, implementation guidelines, legislation for design process, product data process, supply chain management, information sharing.
Here is listed a some of those existing ones that we are considering at our development work.

## Slide 10
Implementation Guideline:
Unique Product Identification and Data Carriers for ETO Products
Previously based on manufacturers’ non-standardised internal codes
A GTIN alone identifies a general product category, not a unique item
Precast elements (ETO products) require a different approach for identification:
  GTIN → identifies the base product type
  MTO variant → identifies the specific variation
  Serial number → distinguishes identical units

## Slide 11
Industry-specific Peppol Implementation guidelines
(Pan-European Public Procurement Online)
Peppol is a network, not a standalone system.
It aims to optimize the supply chain, not create a single central point.
Based on the international standard ISO/IEC 19845:2015 (UBL).
Already used in the construction industry in several Nordic countries.
Each country may have its own Peppol Authority responsible for national governance.
To connect to the Peppol network, organizations need an authorized Peppol service provider and a compatible system (e.g., order management or ERP system).
Service Metadata Provider (SMP), Service Metadata Locator (SML)
NOT STANDARDISED
Peppol STANDARDISED
REGULATED
CORNER 1
SUPPLIER
(SENDER)
CORNER 4
BUYER
(RECEIVER)
CORNER 2
Peppol
service
provider
CORNER 3
Peppol
service
provider
CORNER 5
Peppol
service
provider
TAX
ADMINISTRATION
DATA VAULT
INVOICE
INVOICE
CLEARED INVOICE
PEPPOL BIS
TAX DATA
PEPPOL BIS
TAX DATA
PEPPOL BIS
SML
SMP
Fig. Peppol, 5-corner model for e-invoicing (2021).
BIS Ordering 3.3
BIS Catalogue With Response 3.1
. . .
BIS Advanced Despatch Advice with Receipt Advice
. . .
Invoice
Work in progress…
Notes: Peppol is an international network that enables the exchange of standardized electronic documents such as catalogues, orders, order confirmations, invoices, and logistics documents.
In Finland, we are developing industry-specific Peppol implementation guidelines.
Currently, we are working on three Peppol Business Interoperability Specifications (BIS) used within the Peppol network:
BIS Catalogue with Response
BIS Ordering
BIS Advanced Despatch Advice with Receipt Advice

## Slide 12
Current State
Development roadmap
Future State
Future State Data Flow Architecture
for Engineer-to-Order Precast Concrete
Our development work follows the TOGAF framework and the national JHS-179 architecture principles to build an industry-level architecture for different production strategies.
The Future State Data Flow Architecture serves as a key representation combining process (action) and data architecture. It illustrates data repositories, interfaces, and core process functions of a digitized supply chain.
The data architecture diagram functions as an evolving artefact throughout the development project.
Notes: Our development work follows the TOGAF framework and the national JHS-179 architecture principles to build an industry-level architecture for different production strategies.
The Future State Data Flow Architecture representation brings together both process and data perspectives. It shows how information moves across the supply chain — the data repositories, interfaces, and core process functions that enable a digital way of working.
This data architecture diagram is not static — it serves as an evolving artefact that develops and matures throughout the project.

## Slide 13
PRODUCT DESIGN
MANUFACTURING
FACILITY MANAGEMENT
CONSTRUCTION
WP
3
WP
1
WP
2
WP
6
WP
4
WP
5
WP
9
WP
7
WP
8
PROCUREMENT
Element Production Plans
Enrichment of the E-BOM into the Manufacturing Bill of Materials (M-BOM)
Catalogue ↑ ↓ Order
Order response↑
Sale
Delivery
SUPPLIERS
Installation of element
(As-built data collection)
Production planning
Acceptance inspection
(Claim if necessary)
Quantity take-off
Product Information DB
(ETIM Classification / TT-standard / EMDG) and product identification (GS1/GTIN)
Purchase
Purchase
Delivery
ID: GTIN/SSCC
    Data Carrier: 1D, 2D barcodes
Information delivery
(if necessary)
Production
ID:(S)GTIN
Data carrier:
1D, 2D barcodes
ERP
(MRP)
Sale
Access Point
Access Point
Despatch advice ↑ ↓ Receipt advice
Invoice ↑ ↓ Invoice response
Access Point
Access Point
DESIGN
Engineering
Bill of Materials
(E-BOM)
ERP
(WMS/MRP/
PIM)
Receiving (collection of product and process data)
Access Point
Access Point
↑ Order response
Access Point
Access Point
Peppol messages:
ERP
Transport arrangement
ID: SGTIN / SSCC
AIDC:
1D, 2D barcodes / RFID
Access Point
Access Point
Peppol-messages:
Receipt advice ↓ ↑ Invoice
Invoice response↓
The client's ERP and property management systems
Query-based data transfer between databases
ERP
CAFM
+
DP
Electronic Transport Documents
(eFTI / eCMR)
Event Data Sharing
(GS1 EPCIS/CBV)
Electronic Transport Documents
(eFTI / eCMR)
Event Data Sharing
(GS1 EPCIS/CBV)
ARC-BIM
(Architectural design)
IFC
Tender↓
Blanket Order↓
↑ Order response
↑ Tendering message . response
Peppol messages:
Order Change↓
Call off order ↓
↑ Despatch advice
↑ Order response
CDE
IFC
Production
UPID: SGTIN
AIDC: 2D barcodes / RFID
Production scheduling
As Scheduled & As Manufactured data collection
Receiving
DP
DPP
DPP
Exchange of structured order-to-delivery messages
N.N
A function or part of a process
Legend
Automatic Identification & Data Capture (AIDC)
1D barcode
GS1-128, EAN
2D barcode
GS1 DataMatrix
GS1 Digital Link
DPP EU Digital product Passport
Peppol
network
eCMR Electronic consignment note
eFTI Electronic freight transport information
N.N
Stakeholder or stage in the production chain
In use
Under development
Information service or platform
CAFM Computer Aided Facility Management
Common Data Environment
(Project Shared data repository)
DP Data Platform
ERP Enterprise Resource Planning
MRP Material Resource Planning
PIM Product Information Management
WMS Warehouse Management System
RFID
Passive UHF RFID
Identification
GTIN Global Trade Item Number
SGTIN Serialized Global Trade Item Number
SSCC Serial Shipping Container Code
Information exchange
IFC
Industry Foundation Classes (IFC) –file format
E-BOM Engineering Bill Of Materials
M-BOM Manufacturing Bill Of Materials
Design / Manufacturing Data
Product information
Process Data (Transaction Data)
Process Data (Transport Data)
EPCIS Electronic Product Code Information Services
CBV Core Business Vocabulary
Process Data (Event Data)
EMDG European Master Data Guideline
CDE
PUBLIC, NON-PROFIT INFORMATION SERVICE
Financial system
PRH: CSRD
EFRAG:XBRL: financial statement and sustainability report
EU: Corporate Sustainability Reporting Directive
Transport CO2 data
CO2 and sustainability reporting data
Project development
Cost modelling
Building Control
The RYTJ (Built Environment Information System) is a national digital system in Finland that collects and provides data on land use planning, construction permits, and the built environment
MEP-BIM
(MEP-design)
STR-BIM
(Structural design)
IFC
IFC
National interoperability platform
koodistot.suomi.fi; tietomallit.suomi.fi; sanastot.suomi.fi
Buildingsmart data dictionary (bsDD)
Reference Data, Terminologies,
Data Vocabularies
Terms, property definitions, classifications, and relationships
used in the built environment.
Reference Data (Product Classifications)
CDE
Rough capacity planning
MRP/WMS
Environmental balance sheet value accounting
Future-State Data Flow Architecture for Engineer-to-Order Precast Concrete
Notes: The Future State Data Flow Architecture shown here represents the stakeholders and stages of the production chain. It includes functions and process components, as well as the information services and platforms that enable data exchange.
The diagram illustrates information exchange interfaces, and core process functions of a digitized supply chain, highlighting product identification.
Also, the exchange of design data, product information, transactional data, transport data, and event data between stakeholders.
Thank you, that was my presentation.